## Slide 1
BD9C601EFJEVK-101 Measurement Report
April 16th, 2014
Hosted by: Xuan Dang

## Slide 2
Equipment list
Regulated DC Power Supply
  QJE QJ3005XE (0-30V/5A)
Multimeter:
  Fluke 87V True RMS
  Fluke 106
Oscilloscope
  Rigol DS1102E
Electronic Load
  B&K BK8500
Current probe
  RP1001C

## Slide 3
Functional Test
Testing procedure
  Turn on the DC Supply. Set output of the DC Supply in range from 4.5V to 18V and turn it off. Connect DC the Supply to: [+]VIN(TP1) and [-]GND(TP2) of evaluation board.
  Connect Electronic Load to: [+]VOUT(TP3) and [-]GND(TP4). Power on Electronic Load, set input of Electronic Load to 6A.
  Turn on the DC Supply.
  Turn on load.
  Move J1 header to turn EN on.
Result:
VIN = 4.5V to 18V
VOUT = 3.22V ~ 3.29V.
Test passed.

## Slide 4
Hot Plugging Test
Test condition
  VIN = 18V
  IOUT = 6A
  With original diode D2: SMAJ15A
Result:
IIN MAX= 76A
VIN peak transient voltage is 22V > VIN Maximum Rating (20V)
ICC quiescent current is 93mA at VIN=18V
The IC still operate properly after 100+ test time.
VIN 5V/Div. (DC)
IIN 20A/Div. (AC)

## Slide 5
Hot Plugging Test (cont.)
Test condition
  VIN = 18V
  IOUT = 6A
  With diode D2: SMAJ18A
Result:
IIN MAX= 78.4A
VIN peak transient voltage is 26.8V > VIN Maximum Rating (20V)
ICC quiescent current is 29mA at VIN=18V
The IC still operate properly after 100+ test time.
VIN 5V/Div. (DC)
IIN 20A/Div. (AC)

## Slide 6
Hot Plugging Test (cont.)
Test condition
  VIN = 18V
  IOUT = 6A
  With diode D2: SMAJ16A
Result:
IIN MAX= 75.2A
VIN peak transient voltage is 23.8V > VIN Maximum Rating (20V)
ICC quiescent current is 26mA at VIN=18V
The IC still operate properly after 100+ test time.
VIN 5V/Div. (DC)
IIN 20A/Div. (AC)

## Slide 7
Hot Plugging Test (cont.)
Test condition
  VIN = 18V
  IOUT = 6A
  With diode D2: SMAJ14A
Result:
IIN MAX= 80A
VIN peak transient voltage is 21V > VIN Maximum Rating (20V)
ICC quiescent current is 200mA at VIN=18V
VIN 5V/Div. (DC)
IIN 20A/Div. (AC)

## Slide 8
Hot Plugging Test (cont.)
Test condition
  VIN = 18V
  IOUT = 6A
  With diode D2: SMAJ13A
Result:
IIN MAX= 82.4A
VIN peak transient voltage is 18.8V < VIN Maximum Rating (20V)
ICC quiescent is 380mA at VIN=18V
VIN 5V/Div. (DC)
IIN 20A/Div. (AC)

## Slide 9
Circuit Quiescent Current Measurement
Test condition
  VIN = 0-18V
  Room temperature 25oC
Chart: VCC (V)

## Slide 10
Efficiency Measurements
Test condition
  VIN = 12V
  VOUT = 3.3V
  With SMAJ15A
  Room temperature 25oC
Chart: IOUT (mA)
| 0 | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000 | 1500 | 2000 | 2500 | 3000 | 3500 | 4000 | 4500 | 5000 | 5500 | 6000
With SMAJ15A | 0 | 49.9 | 66.5 | 74.5 | 79.3 | 83 | 84.3 | 85.5 | 86.7 | 87.6 | 88.7 | 89.9 | 89.6 | 89.1 | 88.8 | 88 | 86.9 | 86 | 84.8 | 83.7 | 82.4

## Slide 11
Load Response Measurements
Load response characteristic
(VIN=12V, VOUT=3.3V, IOUT=0  6A)
VOUT 300mV/Div. (AC)
IOUT 3A/Div. (DC)

## Slide 12
Load Response Measurements (cont.)
Load response characteristic
(VIN=12V, VOUT=3.3V, IOUT=6A  0)
VOUT 300mV/Div. (AC)
IOUT 3A/Div. (DC)

## Slide 13
Ripple Response Measurements
VOUT Ripple voltage
(VIN=12V, VOUT=3.3V, IOUT=6A)
VSW 5V/Div. (DC)
VOUT 20mV/Div. (AC)

## Slide 14
Ripple Response Measurements (cont.)
VOUT Ripple voltage
(VIN=12V, VOUT=3.3V, IOUT=0A)
VSW 5V/Div. (DC)
VOUT 20mV/Div. (AC)

## Slide 15
Input Voltage Ripple Measurements
VIN Ripple voltage
(VIN=12V, VOUT=3.3V, CIN=10uF+ 0.1uF, IOUT=6A)
VIN 200mV/Div. (AC)

## Slide 16
Input Voltage Ripple Measurements (cont.)
VIN Ripple voltage
(VIN=12V, VOUT=3.3V, CIN=10uF + 0.1uF, IOUT=0A)
VIN 50mV/Div. (AC)